## Slide 1
Congestion Control
Notes: 1

## Slide 2
2
Outline
Reacting to Congestion
Avoiding Congestion
Queuing Discipline
Notes: 2

## Slide 3
3
Issues
Congestion Avoidance vs Control:
  pre-allocate resources so as to avoid congestion (avoidance)
  control congestion if (and when) it occurs (control)
Underlying service model
  best-effort (assume for now)
  multiple qualities of service (later in CS 6390)
Destination
1.5-Mbps T1 link
Router
Source
2
Source
1
100-Mbps FDDI
10-Mbps Ethernet
Notes: 3

## Slide 4
4
Evaluation
Fairness – allocate resources fairly among flows.
Power (ratio of throughput to delay)
  If you increase load too much
    Packet losses increase
    Queuing delay increases
Optimal
load
Load
Throughput/delay
Notes: 4

## Slide 5
5
Taxonomy of schemes
Point of implementation
  router-centric versus host-centric (TCP)
Resource allocation scheme
  reservation-based
  feedback-based
    explicit
    implicit (TCP)
Rate control Method
  window-based (TCP)
  rate-based
Notes: 5

## Slide 6
6
TCP Congestion Control
Idea:
  assumes best-effort network (FIFO or FQ routers)
  each source determines network capacity by itself
    uses implicit feedback
  ACKs pace transmission (self-clocking sliding window)
Challenges:
  determining the available capacity in the first place
  adjusting to changes in the available capacity
Notes: 6

## Slide 7
Self-clocking or ACK Clock (picture of bottleneck router link)
Pr
Pb
Ar
Ab
Receiver
Sender
As
Self-clocking systems tend to be very stable under a wide range of bandwidths and delays.
The principal issue with self-clocking systems is getting them started.
Notes: 7
Implications of ack-clocking:
  More batching of acks => bursty traffic
  Less batching leads to a large fraction of Internet traffic being just acks (overhead)

## Slide 8
8
Throughput
If the window is W
And if the round-trip delay is D
What is the throughput of TCP?
  (assuming the “bottleneck” link is not the first link of the host)
Source
Dest
Router
Router
Router
Router
One of these routers is the “bottleneck” router, whose link is the slowest (or busiest)
Notes: 8

## Slide 9
Window vs Round-Trip-Time
9
How would you adjust the window?
Wopt = optimum window = baseRTT * Bandwidth
Notes: 9

## Slide 10
Window vs Throughput
10
How would you adjust the window?
Notes: 10

## Slide 11
TCP
TCP does NOT know what baseRTT is (the network does not tell it) nor the bandwidth!
So, it CAN’t compute Wopt!
It must therefore act “blind”
11

## Slide 12
12
AIMD (cont)
Question: how does the source determine if the network is congested?
Notes: 12

## Slide 13
13
AIMD (cont)
Question: how does the source determine if the network is congested?
Answer: a timeout occurs (or a fast retransmit)
  timeout signals that a packet was lost
  packets are seldom lost due to transmission error
  lost packet implies congestion
Notes: 13

## Slide 14
14
AIMD (cont)
How does the source determine the network is NOT congested?
Notes: 14

## Slide 15
15
AIMD (cont)
How does the source determine the network is NOT congested?
  You can’t, you just assume it is !!!
Notes: 15

## Slide 16
16
Additive Increase/Multiplicative Decrease
Objective: adjust to changes in the available capacity
New state variable per connection: CongestionWindow
  limits how much data source has in transit
MaxWin = MIN(CongestionWindow, AdvertisedWindow)
(LastByteSent - LastByteAcked) ≤ MaxWin
Idea:
  increase CongestionWindow when congestion goes down
  decrease CongestionWindow when congestion goes up
Notes: 16

## Slide 17
17
AIMD (cont)
Algorithm
  increment CongestionWindow by one packet per RTT (additive increase)
  divide CongestionWindow by two whenever a timeout occurs (multiplicative decrease)
Source
Destination
…
In practice: increment a little for each ACK
Increment = MSS * (MSS/CongestionWindow)
CongestionWindow = CongestionWindow + Increment
Notes: 17

## Slide 18
18
AIMD (cont)
Trace: sawtooth behavior
60
20
1.0
2.0
3.0
4.0
5.0
6.0
7.0
8.0
9.0
KB
T
ime (seconds)
70
30
40
50
10
10.0
Notes: 18

## Slide 19
Why AIMD?
Think fairness
19

## Slide 20
AIMD is sensibly fair
20

## Slide 21
21
Initial window value
Initially, you don’t know the network capacity
What then should be the value of congwin?
  Perhaps a value hard-coded in the program:
    E.g., always start W = 20KB
Problems:
  If congwin is too small, we waste bandwith
    Takes a long time for congwin to grow using cong. avoidance
  If congwin is too big we cause congestion
  Dumping congwin bytes in the network, at once, even if W is the right value, may cause congestion.
Notes: 21

## Slide 22
22
Slow Start
Objective: determine the available capacity in the first place
Idea:
  begin with CongestionWindow = 1 packet
  double CongestionWindow each RTT (increment by 1 packet for each ACK)
Source
Destination
…
Notes: 22

## Slide 23
23
time
cwnd
When to switch to linear? There is no good answer when you startup a connection

## Slide 24
24
Slow Start (cont)
Exponential growth, but slower than all at once
Used…
  when first starting connection
  when connection goes dead waiting for timeout and we go into congestion control (see next slides)
    By the way, how many of your packets are in the network after you receive an ack for a retransmitted packet?
Notes: 24

## Slide 25
25

## Slide 26
26

## Slide 27
27

## Slide 28
28
250

## Slide 29
29

## Slide 30
30
Congestion Control
After a timeout, we are in “congestion control” mode
  set slow-start threshold SSThresh to CongestionWindow/2
  set CongestionWindow to 1
Allow CongestionWindow to grow exponentially using “slow start” until it reaches the SSThresh
Then, continue with additive increase of CongestionWindow (i.e., back to congestion avoidance)
Notes: 30

## Slide 31
Window size over time
31
time
cwnd
0
2
4
6
8
10
12
14
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Transmission round
congestion window size
(segments)

## Slide 32
32
Fast Retransmit
Problem: coarse-grain TCP timeouts lead to idle periods
Fast retransmit: use duplicate ACKs to trigger retransmission (3 of them in case there is reorder)
Packet 10
Packet 20
Packet 30
Packet 40
Packet 50
Packet 60
Retransmit
packet 30
ACK 20
ACK 30
ACK 30
ACK 30
ACK 70
ACK 30
Sender
Receiver
Notes: 32

## Slide 33
33
Slow start or not?
After a fast retransmission –
  Do a slow start? (set the CongestionWindow to 1 and increase exponentially up to Thresh)
    (again, how many packets are in the network after we receive an ack for the retransmitted packet?)
  Or not? (Fast Recovery, details later…)
    Go “directly” to half the previous congestion window
    Avoid the slow start
    More details on this later …
The above depends on the version of TCP
Notes: 33

## Slide 34
TCP Tahoe and TCP Reno (for single segment losses)
Reno
time
cwnd
time
cwnd
Tahoe
Does slow start
Does “fast recovery”
Notes: 34

## Slide 35
35
Summary: TCP Congestion Control
When CongWin is above SShreshold, sender is in congestion-avoidance phase, window grows linearly.
When timeout occurs (i.e., congestion), SSThreshold set to CongWin/2 and CongWin is set to 1 MSS (i.e. slow-start)
When CongWin is below SSThreshold, sender in slow-start phase, window grows exponentially.
When a fast retransmission (i.e., congestion) occurs,
  If fast recovery not implemented, then slow the same as a timeout.
  if fast recovery, then we stay in congestion-avoidance (details follow)
Notes: 35

## Slide 36
36

## Slide 37
37

## Slide 38
38

## Slide 39
39

## Slide 40
40

## Slide 41
41

## Slide 42
42
Fast Recovery, more details
Assume we have the following scenario (10 byte packets)
  100 segments 10, 20, 30, … 990, 1000 have been sent,
  cwnd = 1000, ssthr ≤ 1000 (congestion avoidance) thus, 100 segments (10 bytes each) are “flying” in the channel
Assume segment 10 is lost
Thus, when segments 20, 30, and 40 are received, the receiver will send 3 duplicate ack(10)
Notes: 42

## Slide 43
43
Fast Recovery (more details)
When the third duplicate ACK(10) in a row is received:
  set ssthreshold to one-half the current congestion window, congwin, but no less than two segments.
    i.e., set ssthreshold = 500
    congwin remains at 1000 (for the moment)
  Retransmit the missing segment.
    Rxmit segment 10
    Notice, “new” 10 is now “behind” segments 1000, 990, 980, … , 50
Notes: 43

## Slide 44
44
Fast Recovery (more details)
NOTE:
  congwin does not allow you to send any more packets (the window is “closed”)
  If you wait for the retransmitted segment 10 to reach the receiver and the ack (which will ack all 1000 bytes) to arrive at the sender, the network will be empty of packets and a slow-start must be performed
    we don’t want this. You want to continue to send data and prevent the network from being empty (recall self-clocking)
  You would need a window of size 1010 before you can send another new packet.
Notes: 44

## Slide 45
45
Fast recovery (contd)
We thus temporarily increase congwin
Set congwin to threshold plus 3 times the segment size.
    congwin = 500 + 30 = 530
    This inflates the congestion window by the number of segments that have left the network and which the other end has received and stored (3).
    It is not big enough yet to transmit new data
Each time another duplicate ACK arrives
  Increment congwin by the segment size.
    This inflates the congestion window for the additional segment that has left the network.
  Transmit a packet, if allowed by the new value of congwin.
    Note that congwin needs to grow to at least 1010 for this to happen.
Notes: 45

## Slide 46
46
Fast recovery (back to the example)
We have congwin = 530, and 96 old segments flying (1000 … 50)
When receiver rcvs segments 510 .. 50 the rcvr sends back duplicate ack(10), i.e., 47 duplicate ack’s.
Each of these will increase the window by 10 at sender
  New congwin = 1000 (as big as before!)
Still have 1000 … 520 outstanding (about ½ old window)
  Note, we can now send new data if more acks come in (because the window will grow)
Notes: 46

## Slide 47
47
Fast recovery (contd)
When segments 1000 … 520 are rcvd, receiver sends 49 duplicate ack(10)
Thus, congwin increases by 490: congwin = 1490
congwin grows from 1000 to 1490
Thus, we can now send segments 1010 … 1490 as the window increases (i.e. 1490, … ,1010, 10, …)
  These are 49 new packets, not retransmissions
  These packets are behind the retransmitted packet 10
Notes: 47

## Slide 48
48
Fast recovery (more details)
When segment 10 arrives at the receiver:
  the send an ack for ALL the data – ack(1010)
  segments still flying: 1490 ..1010
    these are the new packets sent after the retransmission
When ack(1010) arrives at the sender
  Fast retransmit is over at this point.
  set congwin to threshold (the value set in step 1).
  congwin = 500
  We can now send segment 1500
We now have congestion avoidance (congwin = thresh) at one-half the rate it was at when the packet was lost (congwin = 500)
Notes: 48

## Slide 49
TCP New Reno
When multiple packets are dropped, Reno has problems
Partial ACK:
  Occurs when multiple packets are lost
  A partial ACK acknowledges some, but not all packets that are outstanding at the start of a fast recovery,
    It takes sender out of fast recovery
    Sender has to wait until timeout occurs (then slowstart)
New Reno:
  Partial ACK does not take sender out of fast recovery (basically, don’t slide the window).
  Partial ACK causes retransmission of the segment following the acknowledged segment
New Reno can deal with multiple lost segments without going to slow start
Notes: 49

## Slide 50
50
Congestion Avoidance
TCP’s strategy
  control congestion once it happens
  repeatedly increase load in an effort to find the point at which congestion occurs, and then back off
Alternative strategy
  predict when congestion is about to happen
  reduce rate before packets start being discarded
  call this congestion avoidance, instead of congestion control
Two possibilities
  router-centric: DECbit and RED Gateways
  host-centric: TCP Vegas
Notes: 50

## Slide 51
51
Random Early Detection (RED)
Notification is implicit
  just drop the packet (TCP will timeout)
  could be made explicit by marking the packet
Early random drop
  rather than wait for queue to become full, drop each arriving packet with some drop probability whenever the average queue length exceeds some drop level
Notes: 51

## Slide 52
52
RED Details
Compute average queue length
AvgLen = (1 - Weight) * AvgLen +
Weight * SampleLen
0 < Weight < 1 (usually 0.002)
SampleLen is queue length each time a packet arrives
MaxThreshold
MinThreshold
A
vgLen
Notes: 52

## Slide 53
53
RED Details (cont)
Two queue length thresholds
if AvgLen ≤ MinThreshold then
enqueue the packet
if MinThreshold < AvgLen < MaxThreshold then
calculate probability P
drop arriving packet with probability P
if MaxThreshold ≤ AvgLen then
drop arriving packet
Notes: 53

## Slide 54
54
RED Details (cont)
Computing probability P
TempP = MaxP * (AvgLen - MinThreshold)/ (MaxThreshold - MinThreshold)
P = TempP/(1 - count * TempP)
count = number of new packets NOT dropped while within MinThresh and MaxThresh
TempP
1.0
MaxP
MinThresh
MaxThresh
A
vgLen
TempP
Notes: 54

## Slide 55
55
Final P
P = TempP/(1 - count * TempP)
count = number of consecutive packets NOT dropped while within MinThresh and MaxThresh
This spreads the losses more over time
E.g., assume:
MaxP = 0.02, count = 0, AvgLen = (MaxThreshold + MinThreshold)/2 TempP = 0.01
Assume AvgLen remains where it is
After 50 packets arrive without dropping
  P = 0.01/(1 – 50*0.01) = 0.02
After 99 packets arrive without dropping
  P = 0.01/(1 – 99*0.01) = 1 !!!
  Packet will be dropped
  Prevents long periods without dropping
Notes: 55

## Slide 56
56
Why RED
Probability of dropping a particular flow’s packet(s) is roughly proportional to the share of the bandwidth that flow is currently getting
  It is fair (or sensibly so)
It keeps the queue size small
  TCP tries to do the opposite, make it big
  Big queue sizes lead to “buffer bloat”
  RED helps to prevent this
Notes: 56

## Slide 57
57
Tuning RED
MaxP is typically set to 0.02, meaning that when the average queue size is halfway between the two thresholds, the gateway drops roughly one out of 100 packets.
If traffic is bursty, then MinThreshold should be sufficiently large to allow link utilization to be maintained at an acceptably high level
Notes: 57

## Slide 58
58
Tuning Red (cont)
Difference between two thresholds should be larger than the typical increase in the calculated average queue length in one RTT;
  I.e., in one RTT windows (throughput) increase, and the drop prob should not jump from 0 to 1.
  setting MaxThreshold to twice MinThreshold is reasonable for traffic on today’s Internet
MaxThreshold should be smaller than the entire buffer size
  We want P = 1 when the average queue size is greater than MaxThreshold ,
  A burst may increase queue size above MaxThreshold,
    This causes all arriving packets to be dropped
    But P != 1, so this is not our intended effect.
Notes: 58

## Slide 59
59
Source-Based Congestion Avoidance
Perhaps the source can detect that congestion is starting to occur (rather than just react when it occurs)
When congestion begins to occur
  Buffers begin to fill up at intermediate routers
  Queuing delays (hence RTT) increases
  Throughput does not increase regardless of how fast we send or how big the window is
    The network cannot send any faster
Notes: 59

## Slide 60
60
TCP plot
Idea: source watches for some sign that router’s queue is building up and congestion will happen too; e.g.,
  RTT grows
  sending rate flattens
60
20
0.5
1.0
1.5
4.0
4.5
6.5
8.0
KB
Time (seconds)
Time (seconds)
70
30
40
50
10
2.0
2.5
3.0
3.5
5.0
5.5
6.0
7.0
7.5
8.5
900
300
100
0.5
1.0
1.5
4.0
4.5
6.5
8.0
Sending KBps
1100
500
700
2.0
2.5
3.0
3.5
5.0
5.5
6.0
7.0
7.5
8.5
Time (seconds)
0.5
1.0
1.5
4.0
4.5
6.5
8.0
Queue size in router
5
10
2.0
2.5
3.0
3.5
5.0
5.5
6.0
7.0
7.5
8.5
Notes: 60

## Slide 61
61
TCP Vegas Algorithm
Let BaseRTT be the minimum of all measured RTTs (commonly the RTT of the first packet)
If not overflowing the connection, then
ExpectRate = CongestionWindow/BaseRTT
Source calculates sending rate (ActualRate) once per RTT
  Send a distinguished packet
  Compute the RTT of this distinguished packet (when its ACK arrives)
  Divide number of bytes transmitted while waiting for the ACK by the RTT measured.
Notes: 61

## Slide 62
62
Algorithm (cont)
Source compares ActualRate with ExpectRate (note: ExpectRate > ActualRate by definition!)
Diff = ExpectRate - ActualRate
if Diff < a
increase CongestionWindow linearly
else if Diff > b
decrease CongestionWindow linearly
else
leave CongestionWindow unchanged
Notes: 62

## Slide 63
63
a and b as “packets”
a and b are defined as rate, i.e., in bytes/sec.
Typically, the throughput varies widely from one connection (destination) to another
  Thus we need a a and b to be related to the throughput of the current connection
They are usually expressed as # of MSS’s divided by baseRTT
  Thus, you can think of a and b as the number of “extra” packets in the network beyond the bandwidth-delay product.
  More on this later
Notes: 63

## Slide 64
64
Algorithm (cont)
Parameters
  a = 1 packet
  b = 3 packets
Even faster retransmit
  keep fine-grained timestamps for each packet
  check for timeout on first duplicate ACK
70
60
50
40
30
20
10
KB
T
ime (seconds)
0.5
1.0
1.5
2.0
2.5
3.0
3.5
4.0
4.5
5.0
5.5
6.0
6.5
7.0
7.5
8.0
0.5
1.0
1.5
2.0
2.5
3.0
3.5
4.0
4.5
5.0
5.5
6.0
6.5
7.0
7.5
8.0
CAM KBps
240
200
160
120
80
40
T
ime (seconds)
Actual rate
Expected rate
Notes: 64

## Slide 65
65
Modified Slow Start
Instead of doubling every RTT, double every other RTT
Keep window the same for one RTT after doubling
Then check for congestion (ab test as above)
If congestion, go to additive increase
Notes: 65

## Slide 66
66
a and b as packets/base_rtt
basertt = minimum rtt seen thus far (probably equal to the minimum possible rtt with little or no queuing delay)
actualrtt = the actual rtt being experienced at this moment
actualrate = W/actualrtt
expectedrate = W/basertt
optimumW = bandwidth delay product = basertt * C, where C is the share of the bandwidth of the network available to the flow.
Notes: 66

## Slide 67
67
a and b as packets/base_rtt
During early stages of congestion, we can claim that C = actualrate
  because if the flow attempts to transmit faster than C, the network will only xmit its packets at a rate of C, all the other packets beyond this will be queued at the router.
  actualrate = C
optimumW = basertt * C = basertt * actualrate = basertt * W / actualrtt
rearranging: W/actualrtt = optimumW/basertt
Notes: 67

## Slide 68
68
a and b as packets/base_rtt
expectedrate - actualrate = W/basertt - W/actualrtt {by definition} = W/basertt - optimumW/basertt {from previous slide} = (W - optimumW)/basertt
Thus, α and β are bounds on (expectedrate - actualrate), and hence, they are bounds on
  (W - optimumW)/basertt
Hence, you can express these bounds in terms of "packets per basertt“
  and, they correspond to the number of extra packets in W compared to the optimum window.
Notes: 68

## Slide 69
69
DECbit : end host behavior
Add binary congestion bit to each packet header
Source sets bit to 0
If congestion, the router will flip the bit to 1
Destination echoes bit back to source in the ack’s
Source records how many packets resulted in set bit
  If less than 50% of last window’s worth had bit set
    increase CongestionWindow by 1 packet
  If 50% or more of last window’s worth had bit set
    Multiply CongestionWindow by 0.875
Notes: 69

## Slide 70
70
DECbit : router behavior
Router monitors average queue length over last busy+idle cycle
set congestion bit if average queue length > 1
attempts to balance throughput against delay
Queue length
Current
time
T
ime
Current
cycle
Previous
cycle
A
veraging
interval
Notes: 70

## Slide 71
71
Queuing Discipline (Scheduling)
First-In-First-Out (FIFO)
  does not discriminate between traffic sources (one queue for all)
Fair Queuing (FQ)
  explicitly segregates traffic based on flows (how?)
  ensures no flow captures more than its share of capacity
  variation: weighted fair queuing (WFQ)
FQ problems:
  How to differentiate between flows
  Must consider variable packet size
Flow 1
Flow 2
Flow 3
Flow 4
Round-robin
service
Notes: 71

## Slide 72
72
Fair Queuing Algorithm
In FQ, there are two “servers” (or systems)
  The real system
    This is the real router with a real output link and the real flows arriving into the router
  The “fake” system
    It does not exist (only used as reference by real system)
    Has the same output link capacity as the real system
    Has the same input flows (with the same packets) as the real system
    However, it is a “bit-by-bit” server (actually, a fluid server), not a packet server.
Notes: 72

## Slide 73
73
The “fake” system
Bit-by-bit round-robin server
  not real service!, i.e. fake!
Suppose a fake clock ticks each time a bit is transmitted from every active flow (i.e., after each round)
  i.e., it is not a real-time clock
Let Lf,i denote the length of (f,i), i.e., ith packet of flow f
Let Sf,i denote the fake time when start to transmit packet i in the fake system
Let Ff,i denote the fake time when finish transmitting packet i in the fake system (regardless of other flows)
Ff,i = Sf,i + Lf,i
Notes: 73

## Slide 74
Computing Sf,i
When does the (fake) server start to transmit first bit of packet (f,i) ? i.e., what is Sf,i?
  if when f,i arrives, server has not finished packet f,(i -1) from f, then immediately after last bit of (f,i–1), i.e., Sf,i = Ff,i-1
  if no current packets queued for this flow, then start transmitting (f,i) when it arrives, i.e., Sf,i = Vf,i
    where Vf,i is the fake time when the packet arrives
Thus: Ff,i = Sf,i + Lf,i = MAX (Ff,i - 1, Vf,i) + Lf,i
74

## Slide 75
75
Calculating V
V is not “real-time”
It grows depending on the number of backlogged flows (flows whose queue is not empty) in the fake server
  Output channel rate is constant
  We tick after transmitting one bit of each flow
  If more flows, then it takes more time to transmit one bit of each flow (the round takes more time)
  Hence, the number of queued flows dictates how fast (with respect to real-time) V grows.
Notes: 75

## Slide 76
76
Virtual time rate changes with backlogged flows
Real time
V(t)
Virtual time of real time t
Backlogged flows at fake server increased
Backlogged flows at fake server decreased
Notes: 76

## Slide 77
77
Calculating V (continued)
Actually, the rate of growth of V “changes” when the set of backlogged flows (i.e. with non-empty queue) changes.
  The rate of growth increases when a flow is no longer queued
  The rate of growth decreases when the queue of a flow becomes non-empty
It is somewhat of a mess to compute it
  We will cover all the gory details later when we discuss weighted fair queuing (WFQ)
Notes: 77

## Slide 78
78
“Real” FQ Server
Packets are sent out according to which one would exit the fake server first. (try to mimic the fake server)
  Note: we don’t know the real-time of when a packet exits the fake server, but we know the fake time.
  Thus, if Ff,i > Fg,j, we know (g,j) exits the fake server before (f,i), and thus is given higher priority
Notes: 78

## Slide 79
“Real” FQ Server (continued …)
When a packet Pf,i is received
  Compute the value Ff,i (this depends on V)
  Insert packet into a priority queue, ordered by F value
When the output channel becomes idle
  Retrieve the packet from the priority queue with least F value
    I.e. the one that would exit first from the fake server.
  Transmit this packet.
79

## Slide 80
80
FQ Algorithm limitations
Want to emulate the behavior of the bit-by-bit server as much as possible
  We want each packet to exit from the real server no later than it exits from the bit-by-bit server
  However, not perfect: can’t preempt current packet, so exit time may be greater (but only by one packet!)
Example
Flow 2
(a) What you want
(b) What you may get instead
Output
Output
F = 8
F = 10
F = 5
F = 10
F = 5
Flow 1
(arriving)
Flow 2
(transmitting)
Flow 1
Notes: 80