## Slide 1: Internetworking

## Slide 2: Internetworking
What is an internetwork?
  Many networks interconnected, but provide the illusion of having a single network
  Each network has its own addressing and routing mechanism.
  To cross from one network to another, you need an additional layer of software to glue everything together (i.e. IP)
ATM
Ethernet
802.11 wifi
Host
Router

## Slide 3: Internetwork properties
You can send a message from any host to any other host in the Internetwork (via intermediate routers)
Supports heterogeneity: Hardware, OS, network type, and topology independent
Scales to global connectivity

## Slide 4: Individual Network Properties
Network (802.11, Ethernet, ATM, etc) properties
  Must be able to transfer messages between any two nodes in the network.
  Preferably must support broadcast
The Internet is the specific global internetwork that grew out of ARPANET

## Slide 5: Internet Protocol (IP)
Network-level protocol for the Internet
Operates on all hosts and routers
Protocol stack at a node has an “hourglass” shape
Modem
ATM
WIFI
Ethernet
FTP
TFTP
NV
HTTP
TCP
UDP
IP

## Slide 6: Internetworking with IP
H1
R1
R2
R3
H2
IP
IP
IP
IP
IP
TCP
TCP
ETH
WIFI
WIFI
PPP
PPP
ETH
ETH
ETH
APPL
APPL
m
th,m
ih,th,m
eh,ih,th,m
m
th,m
ih,th,m
eh,ih,th,m
WIFI,ih,th,m
ppph,ih,th,m

## Slide 7: Internet Protocol (IP)
Service Model
  Provides datagram service to the transport layer (TCP, UDP)
  Provides global name (and address) space
  Host-to-host connectivity (connectionless)
  Best-effort packet delivery
Not in IP service model
  Delivery guarantees on bandwidth, delay or loss
Delivery failure modes
  Packet delayed for a very long time
  Packet loss
  Packet delivered more than once
  Packets delivered out of order

## Slide 8: Simple Internetworking with IPv4
Topics:
Host addressing
Forwarding
Fragmentation and reassembly
Error reporting/control messages
Host configuration

## Slide 9: IPv4 Address Model
Properties
  32-bit address
  Hierarchical
    (network, host) hierarchy
    Each network has a unique id in the world
    Each host within each network has a unique id within the network.
  An address points to a unique network adaptor
    Hosts have (typically) one IP address
    Routers have multiple IP addresses, one per attached network

## Slide 10: Internetworking
Network 3
Network 1
Network 2
(1,6)
(2,1)
(1,3)
(3,4)
(1,2)
(1,5)
(1,1)
(3,2)
(3,1)
(3,6)
(3,5)
(1,4)
(2,2)
(3,3)
(2,3)
(2,4)
(2,5)

## Slide 11: IP address vs “physical address”
IP addresses have nothing to do with the particular network (e.g. wifi, Ethernet, etc) addresses
    They are typically assigned by the system administrator
Actually, the Ethernet software (driver) in your computer knows nothing (nor cares) about IP and about IP addressing.
    These are typically hardcoded in the hardware of your machine.

## Slide 12: Three Class Model
0
Network (7 bits)
Network (14 bits)
1
1
0
1
0
Network (21 bits)
Host (24 bits)
Host (16 bits)
Host (8 bits)
Class A:
Class B:
Class C:

## Slide 13: IPv4 Address Model
Class | Network ID | Host ID | # of Addresses | # of Networks
A | 0 + 7 bit | 24 bit | 224-2 | 128
B | 10 + 14 bit | 16 bit | 65,536 - 2 | 214
C | 110 + 21 bit | 8 bit | 256 - 2 | 221
D | 1110 + Multicast Address |  | IP Multicast | 
E | Future Use |  |  | 

## Slide 14: IP Packet Format
V
ersion
HLen
TOS
Length
Ident
Flags
Offset
TTL
Protocol
Checksum
IP SourceAddr
IP DestinationAddr
Options (variable)
Pad
(variable)
0
4
8
16
19
31
Data

## Slide 15: IPv4 Addresses in different “forms”
IP addresses
  Decimal-dot notation (turn each byte into decimal)
  Host in class A network
    56.0.78.100 www.usps.gov
  Host in class B network
    128.174.252.1 www.cs.uiuc.edu
  Host in class C network
    198.182.196.56 www.linux.org
Internet domain names
  ASCII strings separated by periods
  Provides some administrative hierarchy
    host.subdomain.domain.domain_type (com, edu, gov, org, …)
    host.domain.country (us, de, jp, …)

## Slide 16: IPv4 Translation support
Internet domain name to IP address (and viceversa)
  Performed by the Domain Name Service (DNS) hierarchy of servers
IP addresses to LAN physical addresses (and viceversa)
  Problem
    An IP route can pass through many physical networks
    Physical (i.e. LAN) network source and destination addresses (at each hop) are needed.
  Solution
    Translate from IP address to physical address
    This is done via the Address Resolution Protocol (ARP)
    IP asks ARP to translate the IP address into a physical address.

## Slide 17: Example
Router (1,2) wants to send an IP message to (1,4)
It must find out the Ethernet address of (1,4) (via ARP)
Then, it gives the IP message and the Ethernet destination address to the Ethernet software (driver).
The Ethernet software encapsulates the IP message and sends it over the Ethernet hardware.
The Ethernet hardware at the other router receives the message.
The Ethernet software decapsulates the message, and gives it to the IP software.
Ethernet
(1,0)
(1,2)
(1,5)
(1,1)
(1,4)

## Slide 18: IP to Physical Address Translation
Hard-coded
  Encode physical address in IP address
  Ex: Map Ethernet addresses to IP addresses
    Makes it impossible to associate IP address with topology (routing becomes too difficult)
Fixed table
  Maintain a central repository and distribute to hosts
    Bottleneck for queries and updates
Automatically (on the fly) generated table
  Use ARP to build table at each host as needed.
  Use timeouts to clean up table (remove unused entries)

## Slide 19: ARP in the Protocol “Stack”
Physical Networks
FTP
TFTP
NV
HTTP
TCP
UDP
IP
ARP

## Slide 20: ARP Request
A wants to send an IP message to B
A broadcasts an ARP-REQUEST message on the physical network
  The ARP-REQUEST is encapsulated into a phys. netw. (e.g. Ethernet) frame
ARP-REQUEST header contains
  sender IP address field = A’s IP address
  sender phys. net. address field = A’s phys. net. address
  target IP address field = B’s IP address
  target phys. net. address field = empty (unknown)
A
B
ARP-REQUEST msg
What does the Ethernet header look like here?

## Slide 21: ARP Reply
All machines in the physical network receive the ARP request
Only B responds, because the target IP address is B’s
B responds with an ARP-REPLY directly to A.
ARP-REPLY header contains:
  sender IP address field = IP address of B
  sender phys. net. address field = phys. net. address of B
  target IP address field = IP address of A
  target phys. net. address field = phys. net. address of A (where does B get this value from?)
A
B
ARP-REPLY msg

## Slide 22: ARP caching
A learned the phys. net. address of B (from the reply)
B also learned the phys. net. address of A (from the request)
All machines on the network will learn A’s phys.net. address (since A’s request was a broadcast) but in general this is not cached.
When a machines learns a new phys. net. address, it keeps it in a cache for future use, to avoid unnecessary ARP messages.
What if no reply from B? A retransmits the request with exponentially increasing intervals (first wait 1 second, then 2 seconds, then 4, etc...)
NOTE: ARP messages DO NOT leave the LAN

## Slide 23: Datagram Forwarding (routing) within IP
Hosts and routers maintain a routing table:
  Contains list of <IP network, next-hop IP address> pairs
  Table is simple and static on hosts
  Table is complex and dynamic on routers
  Often contains a default route
    Pass unknown destination up the hierarchy to the next level
How to forward a packet to its destination.
  Send directly to destination node if the destination is on one of my networks.
  Send indirectly (via another router) to destination if the destination is located on a different network
    To which router? compare network portion of destination address with <network, next hop> pairs in table to find next-hop-router
  Use ARP to get hardware address of host/router

## Slide 24: IP Message Transmission
WiFi
Ethernet
FDDI

## Slide 25: IP Message Transmission
Assume H1/TCP
  Already knows H2’s IP address
  It creates a packet for H2
H1/IP
  Notices H2 is on a different network, so
  forwards packet to its default router R
  To do so, it looks up R’s WIFI address (via ARP) and sends packet to R
R/IP
  R notices H2 is on the same network
  R/IP looks up H2’s Ethernet address (via ARP) and sends the packet
H1
WIFI
R
WIFI
Ether
H2
EtherI
IP
IP
IP
TCP
TCP

## Slide 26: IP Message Transmission
R1
Assume R1 receives an IP msg for H2
  H2 is not in any network of R1
  R1 looks at its routing table
  Its next hop to H2’s network is R2
  R1 looks up R2’s WIFI address using ARP via WIFI
  R1 encapsulates the IP packet into a WIFI packet and sends it to R2
  Etc… (R2 behaves then like in the previous slide)
R2
WIFI
Ether
H2
Ether
IP
IP
TCP
Ether
WIFI
IP

## Slide 27: IP Packet Format
V
ersion
HLen
TOS
Length
Ident
Flags
Offset
TTL
Protocol
Checksum
IP SourceAddr
IP DestinationAddr
Options (variable)
Pad
(variable)
0
4
8
16
19
31
Data

## Slide 28: IP Packet Format
4-bit version
  IPv4 = 4, IPv6 = 6
4-bit header length
  Counted in words, minimum of 5
8-bit type of service field (TOS)
  Originally defined for QoS using Differentiated Services
  Now mostly used for prioritizing routing control messages over normal IP traffic
16-bit total length
  Counted in bytes

## Slide 29: IP Packet Format
Fragmentation support (later)
  16-bit packet ID (IP increments it with each new packet it creates, a.k.a. datagram)
    All fragments from the same datagram have the same ID
  3 single-bit flags
    One of them marks the last fragment
  13-bit fragment offset into datagram
    Counted in words
8-bit time-to-live field (TTL)
  Hop count decremented at each router
  Packet is discard if TTL = 0

## Slide 30: IP Packet Format
8-bit protocol field
  TCP = 6, UDP = 17
16-bit IP checksum on header (not the data)
32-bit source IP address
32-bit destination IP address
Options (variable sized)
  Source-based routing
  Record route
Padding
  Fill to 32-bit boundaries

## Slide 31: IP Fragmentation and Reassembly
Problem
  Different physical layers provide different limits on frame length
    Maximum transmission unit (MTU)
  Source host does not know minimum value of MTU
    Especially along dynamic routes
Solution
  When necessary, split IP packet into acceptably sized packets prior to sending over physical link
  Questions
    Where should reassembly occur?
    What happens when a fragment is damaged/lost?

## Slide 32: IP Fragmentation and Reassembly
Fragments are self-contained IP packets
Reassemble at destination to minimize refragmentation
Drop all fragments in packet if one or more fragments are lost
Avoid fragmentation at source host
  Transport layer (TCP/UDP) should send packets small enough to fit into one MTU of local physical network
  Must consider IP header

## Slide 33: IP Fragmentation and Reassembly
ETH
IP
(1400)
FDDI
IP
(1400)
PPP
IP
(376)
PPP
IP
(512)
PPP
IP
(512)
ETH
IP
(376)
ETH
IP
(512)
ETH
IP
(512)
Start of header
Ident = x
0
Offset 0
Rest of header
1400 data bytes
Start of header
Ident = x
1
Offset 0
Rest of header
512 data bytes
Start of header
Ident = x
1
Offset 512/8
Rest of header
512 data bytes
Start of header
Ident = x
0
Offset 1024/8
Rest of header
376 data bytes
H1
R1
R2
R3
H2
ETH
FDDI
PPP
ETH

## Slide 34: Host Configuration
What configuration information does a host need?
  Its IP address (leased for certain duration)
  Subnet mask (later)
  Default router IP address
  DNS Server IP address
We would like to have management and sharing of IP addresses
  Servers manage a finite number of IP addresses
  Addresses are leased to clients for finite leases
  Renew lease if you need IP address longer
Implementation by the DHCP protocol

## Slide 35: Dynamic Host Configuration Protocol (DHCP)
A simple way to automate configuration information
  Network administrator does not need to enter host IP address by hand
  Good for large and/or dynamic networks

## Slide 36: DHCP
DHCP
relay
DHCP
server
Unicast to server
Broadcast
Host
Other Networks
  DHCP is layered on top of UDP (a simple transport protocol)
When a host powers on, it sends a DHCPDISCOVER message (IP dest. address 255.255.255.255, Ethernet dest. addr all 1’s)
  DHCPDISCOVER contains the host’s physical address
  Either the DHCP server (if located in the same network as the host) or a DHCP relay agent receives the message
    If DHCP relay agent, it forwards the message to the DHCP server
Server replies with an IP number and configuration information
What happens if a host turns itself off without releasing the address?

## Slide 37: DHCP
DHCP
relay
DHCP
server
Unicast
Broadcast
Host
Other Networks
DHCPDISCOVER (looks for server)
  Host broadcasts a DHCPDISCOVER
  Relay unicasts the DHCPDISCOVER to server
DHCPOFFER (server offers IP address)
  Server unicasts DHCPOFFER to relay’s IP address
  Relay broadcasts DHCPOFFER to host
DHCPREQUEST (hosts requests offered IP address)
  Host broadcasts DHCREQUEST
  Relay unicasts DHCPREQUEST to server
DHCPACK (server acks, i.e. grants, IP address)
  Server unicasts DHCPACK to relay’s IP address
  Relay broadcasts DHCPACK to host
Why always broadcast?
Why four messages?

## Slide 38: From Microsoft’s web site
Ethernet/IP broadcasts are used to let other servers (if any) know of the exchange
occurring between the host and the server.
What if the IP Dest address were all zeroes? The Ethernet is broadcast anyway!

## Slide 39: Internet Control Message Protocol (ICMP)
IP companion protocol
  Handles error and control messages
Modem
ATM
FDDI
Ethernet
FTP
TFTP
NV
HTTP
TCP
UDP
IP
ICMP

## Slide 40: ICMP
Error Messages (sent back to the source)
  Host unreachable
  Reassembly failed
  IP checksum failed
  TTL exceeded (packet dropped)
  Invalid header
Control Messages
  Echo/ping request and reply
  Route redirect

## Slide 41: Virtual Private Networks
A VPN is a group of connected networks
Connections between these networks may be over other networks not belonging to the group (e.g. over the Internet)
  E.g., joining the networks of several branches of a company into a “private internetwork”
Goal
  Controlled connectivity
  Unified management/services.

## Slide 42: Virtual Private Networks
C
A
B
M
K
L
C
A
B
M
K
L

## Slide 43: Tunneling
IP Tunnel
  Virtual point-to-point link between an arbitrarily connected pair of nodes
Network 1
Network 2
Internetwork
R1
R2
IP Tunnel
IP Dest = 2.x
IP Payload
IP Dest = 10.0.0.1
10.0.0.1
IP Dest = 2.x
IP Payload
IP Dest = 2.x
IP Payload

## Slide 44: Tunneling
Advantages of tunneling
  Transparent transmission of packets
    The data carried may not even be IP messages!
  Only need to change relevant routers (end points)
    All other nodes think all the branches are in the same location!
  Coupled with encryption, gives you a secure private internetwork.
  End-points of tunnels my have features not available in other Internet routers.
    Multicast, unified routing protocol across all branches.
    Local (private) Addresses
  Useful for mobile routing (mobile IP)
Disadvantages
  Increases packet size
  Processing time needed to encapsulate/decapsulate packets
  Management at tunnel-aware routers