## Slide 1: Routing
Distance Vector

## Slide 2: Routing
Definition
  The task of constructing and maintaining the forwarding table in datagram routing
Goals
  Obtain the “best” path from each node to each other node.
Conceptually
  We will describe the algorithm for a general graph of nodes and edges. We will adapt it to the Internet model at the end (remind me!)

## Slide 3: Routing
Factors
  Network topology can change
  Traffic conditions can change
    What was a “best path” before no longer is!
Desired Properties
  Correctness
  Simplicity
  Robustness
  Find paths with
    High throughput
    Low end-to-end latency

## Slide 4: Routing: Ideal Approach
Maintain information about each link
Calculate “fastest path” between each directed pair
A
C
B
D
G
F
E
For each direction of each link, maintain:
Available bandwidth
Propagation delay
Queuing delay

## Slide 5: Routing: Ideal Approach
Problems
  Unbounded amount of information
    Queuing delay can change rapidly
    Graph connectivity can change rapidly
Solution
  Dynamic
    Periodically recalculate routes
  Distributed
    No single point of failure
    Reduced computation per node
  Abstract Metric
    “Distance” may combine many factors (we assume a simple cost)
    Use heuristics to map multiple factors into a single “distance” (or cost)

## Slide 6: Routing Overview
Algorithms
  Static shortest path algorithms (network graph is given)
    Bellman-Ford
      Based on comparing information with neighboring nodes
    Dijkstra’s algorithm
      Build tree from source to all other nodes
  Distributed, dynamic routing algorithms (graph is “discovered”)
    Distance vector routing
      Distributed form of Bellman-Ford
    Link state routing
      Distributed Dijkstra’s algorithm

## Slide 7: Bellman-Ford Algorithm
Static centralized algorithm (i.e., not used directly in a network)
Given
  Directed graph with edge costs and a destination node
Finds
  Least cost path from each node to a specific destination
Multiple destination nodes ???
  To find shortest paths for multiple destination nodes, run entire Bellman-Ford algorithm once per destination

## Slide 8: Bellman-Ford Algorithm
I will assume (for simplicity) an undirected graph (i.e. cost is the same in both directions of an edge).
  You can figure out the general case where each edge has different cost in its two directions.
Initially every node is labeled with
  its “current” cost to the destination
  its “current” choice of next-hop.
Note, initially no one knows how to reach the destination 

## Slide 9: Bellman-Ford Algorithm
A
D
B
E
C
Destination





5
1
6
2
1
2
1

## Slide 10: Bellman-Ford Algorithm
Based on iterations,
  each iteration visits every pair of nodes joined by a link
One iteration is of the form:
  for every node A and
    for every neighbor B of A
      is the cost of the path (A  B    destination) smaller than the current cost from A to the destination?
      if YES
        Make B the next hop node for A
        Update cost from A to destination (from B’s info)

## Slide 11: When to update?
Asynchronously: change cost of each node as you iterate
Synchronously: change the cost of each node only at the end of the iteration
  I do synchronous one on the slides
  Makes the powerpoint easier 
Both end up with the same result anyway

## Slide 12: Bellman-Ford Algorithm (synchronous)
A
D
B
E
C
Destination








1 Dest
5 Dest

3 C
1 Dest
7 E
5 Dest
8 D
3 C
1 Dest
7 E
4 B
8 D
3 C
1 Dest
6 E
4 B
7 D
3 C
1 Dest
6 E
4 B
5
1
6
2
1
2
1

## Slide 13: How to make this distributed?
Each node knows the cost of the link to each neighbor
Each node periodically sends a message to all its neighbors indicating its current cost to the destination (one scalar value if only one destination)
  These messages are NOT synchronized, each node sends them basically at its own pace.
From these messages, each node chooses the next hop according to the least cost of (link cost + neighbor’s cost).
If we want to find a next hop to ALL destinations, we have to send a vector with the cost (a.k.a. distance) to each destination (hence the name, distance vector)

## Slide 14: Distance Vector Routing
Distributed dynamic version of Bellman-Ford
Each node maintains two tables (vectors)
  routing table of <destination, next-hop> pairs
  cost (distance) table of <destination, cost> pairs
Information acquisition
  Assume nodes initially know cost to each neighbor
    Initially, what is your cost to a non-neighbor????
  Each node sends its cost table (vector) to all its neighbors
    Periodically – every 30 seconds, or couple of minutes
NOTE: you don’t need to send your routing table, only your cost table.

## Slide 15: DV Code
NID is the set of all node ID’s
Each node maintains two arrays
rtb : array [NID] of G, {routing table, G is the set of neighbors}
cost : array [NID] of integer, {cost to reach each node}
rtb and cost are implemented as a set of pairs
  otherwise, they would be too large (e.g., 2GB if NID is 4 bytes long)
If there is no pair for destination d, we simply write
  cost[d] = ∞
  rtb[d] = (irrelevant, since cost[d] = ∞)

## Slide 16: Code: declarations
node p
inp
G : set {g | g is a neighbor of p}
up : array [G] of boolean, {is my neighbor up}
var
rtb : array [NID] of G, {routing table}
cost : array [NID] of integer, {cost to reach each node}
d : NID, {temporary variable}
c : array [NID] of integer {temporary variable}
param
g: element of G {g can be any neighbor}

## Slide 17: Code: actions (data)
begin
event: receive data(d) from g
resp:
if d = p then skip {arrived}
else if d  p  cost[d] <  then send data(d) to node rtb[d]
else if d  p  cost[d] =  then skip {non reachable}
end if

## Slide 18: Code: send distance vector action, and detect down neighbors action
event: true {at anytime, send cost to all neighbors}
resp:
if up[g] then send update(cost) to node g
end if
event: ~up[g] {has the neighbor died?}
resp:
for every d do
if rtb[d] = g then cost[d] = 
end if
end for

## Slide 19: Code: receive distance vector
event: receive update(c) from g then
resp: {compare costs to all destinations}
for every d do {for every destination, compare c[] and cost[] }
if d = p then cost[p] := 0
else if d  p 
(rtb[d] = g  cost[d] > c[d] + 1)
then
rtb[d] := g;
cost[d] := c[d]+1 {I assume link cost of 1 for simplicity}
end if
end for
end {code}

## Slide 20: When to choose neigh. g as next hop to d?
2. cost[d] > c[d] + 1
Neighbor g gives me a better (shorter) path, so g becomes next hop to d.
1. rtb[d] = g
I must believe the cost that g tells me since g is my next hop to d
For each destination d, when to do the following? rtb[d] := g (choose my neighbor as my next hop) cost[d] := c[d] + 1 (set my cost to my neighbor’s cost + 1) (an arrow indicates the current routing table entry for d)

## Slide 21: Integer costs
The code above assumes the cost of each link is just 1
I.e., it performs minimum-hop routing
It is easy to change it to the case where the cost of each link is some integer (determined locally by the node).

## Slide 22: Recover from link failure (destination = G, min-hop routing)
A
C
B
D
G
F
F detects that link to G has failed
  F sets its distance to G to infinity and sends a periodic update to A
  A sets its distance to G to infinity and sends a periodic update to C, F, B
C has a hop-count of 2 to G via D
  it thus ignores A’s update
A receives periodic update from C with 2-hop path to G
  A sets distance to G to 3 and send update to F, C, B
F decides it can reach G in 4 hops via A
Destination
(?? What is the next hop from each node to G ??)

## Slide 23: Options
Optional: Triggered Updates
  Resend the cost vector whenever a significant change occurs
    A neighbor has failed
      All costs where this neighbor was a next hop become infinity.
      BTW, how do you detect the failure of a node?
    The cost to a destination changes significantly
      Caused by a significant increase in the cost of the link or the cost advertised by the next hop.
Optional: remember the last update from each neighbor
DVR used in
  Original ARPANET (until 1979)
  Early Internet: Routing Information Protocol (RIP)
  Early versions of DECnet and Novell IPX

## Slide 24: Good news travel quickly
Assume for simplicity that the edge cost = 1 for all edges
consider only node A as the destination.
Assume triggered updates (in addition to periodic updates) sent when any change occurs
A
B
C
D
E
cost
to reach
A
2nd step
3rd step
4th step
5th step
1st step
0 |  |  |  | 
0 | 1 |  |  | 
0 | 1 | 2 |  | 
0 | 1 | 2 | 3 | 
0 | 1 | 2 | 3 | 4
Without triggered updates its identical, just slower

## Slide 25: Bad news may travel slowly (count to )
(A, B) goes down.
Assume nodes remember earlier neighbor reports
 denotes next-hop neighbor to A..
B sees the link is down, recalls that C = 2, and points to C with cost 3
0 | 1  | 2  | 3  | 4 
0 | 3  | 2  | 3  | 4 
0 | 3  | 4  | 3  | 4 
0 | 5  | 4  | 5  | 4 
0 | 5  | 6  | 5  | 6 
0 | 7  | 6  | 7  | 6 
X
A
B
C
D
E
cost
to reach
A
We then continue to send triggered updates
B remembers C’s cost of 2, and sends triggered update
B notices link is down
Triggered updates or not we get the same
result

## Slide 26: Bad news may travel slowly (count to )
Assume nodes don’t remember earlier reports
Assume only periodic updates; no triggered updates
Same as before, except that C sends periodic update to B before B sends it to C.
0 | 1  | 2  | 3  | 4 
0 | 3  | 2  | 3  | 4 
0 | 3  | 4  | 3  | 4 
0 | 5  | 4  | 5  | 4 
0 | 5  | 6  | 5  | 6 
0 | 7  | 6  | 7  | 6 
X
A
B
C
D
E
cost
to reach
A
B receives C’s cost of 2
B notices link is down

## Slide 27: Bad news may travel slowly (count to )
Assume nodes don’t remember earlier neighbor reports, assume triggered updates
B sees the link is down, sets cost = , and assume C sends its periodic update to B (with cost 2) at the same time B sends its triggered cost of  to C.
X
A
B
C
D
E
0 | 1  | 2  | 3  | 4 
0 | 3  |   | 3  | 4 
0 |   | 4  |   | 4 
0 | 5  |   | 5  |  
0 |   | 6  |   | 6 
0 | 7  |   | 7  |  
cost
to reach
A
Initially
B receives periodic update from C while sending  to C

## Slide 28: Distance Vector Routing
General Problem A --- B  C
  Node B notices that its link to A is broken (or is much worse in cost)
  Other nodes (C) believe that the route through B is still good
  B believes the routes of others (C) are still good (even though they go through B)
  Mutual deception!

## Slide 29: Distance Vector Routing
Heuristics for breaking loops
  Set infinity to 16
    Small limit allows fast completion of “counting to infinity”
    Limits the size of the network
  Split horizon
    Avoid counting to infinity by solving “mutual deception” problem
  Split horizon with poisoned reverse
    “Poison” the routes sent to you by your neighbors

## Slide 30: Split Horizon
Avoid counting to infinity by solving “mutual deception” problem.
When C sends an update to node B, it does not include destinations that C routes through B
C
B
A
update(cost)
A is not included in the list of pairs of “cost”
rtb[A]=B

## Slide 31: Split Horizon (continued …)
If B thinks the route is not through C, B will not point to C (no loop is formed!) since C does not offer a route.
If B thinks route is through C (loop already exists), B will timeout (doesn’t receive information from C) and removes the route eventually
      Note that in this case, C does not receive information from B either !!!
C
B
A
update(cost)
A is not included in the list of pairs of “cost”
rtb[A]=B

## Slide 32: Split Horizon and “Poisoned Reverse”
Distance Vector with Split Horizon and Poisoned Reverse:
  When C sends updates to node B, destinations that C routes through B are sent with a distance of infinity
  It’s faster: you don’t need to wait for B to timeout
C
B
A
update(cost)
cost[A] = ∞
rtb[A]=B

## Slide 33: Another example (destination Z)
Assume updates are not triggered (only periodic)
Assume you don’t remember earlier updates from neighbors
Assume S. H. with P. R.
What is the steady state?
What is the best and the worst that can happen to the route to Z if the link from X to Y changes in cost from 10 to 1000?
What if you DO remember your neighbor’s earlier cost?
Z
Y
X
a
b
c
10
10
100
10
10
10
10
10
10
10
10
10 1000

## Slide 34: Please view additional PDF slides
I have another scenario here SH with PR fails.
You don’t have to go through it but it is quite illustrative.

## Slide 35: Distance Vector Routing
Problem
  Information propagates slowly
    One period per hop for new routes (mitigated if we do triggered updates)
    Count to infinity to detect lost routes