## Slide 1: Global Internet
Dealing with complexity and scale

## Slide 2: Need for More Scalability
Even with subnetting (and CIDR which we cover later), it is not scalable enough
For a routing protocol to work, all routers in a network are aware of all other routers in the network
My router here in UTD should not need to know about or talk to routers in Hong Kong.
We need to break the Internet into pieces, or “routing domains”

## Slide 3: Autonomous Systems (Routing Domains)
The Internet is subdivided into Autonomous Systems
There are currently about 13000 active ASM’s
Based on notion of autonomy of control
E.g.: company, university, etc
Each AS has a unique 16 bit ID

## Slide 4: AS Picture and meta picture
Enables hierarchical aggregation of routing information
An entire AS may be viewed as a single “node”
A “meta” routing protocol finds paths from one AS to another
R1
Autonomous system 1
R2
R3
Autonomous system 2
R4
R5
R6
R7
Autonomous system 3
R8
R9
R10
AS1
AS2
AS3

## Slide 5: Autonomous Systems
Intradomain Routing (within an AS)
  Performed using domain-specific algorithm
    Selected by domain administrators
    Allows heterogeneous interior gateway protocols
    E.g. RIP (distance vector), OSPF (link-state), etc.
Interdomain Routing (between ASMs)
  Performed using standard global algorithm
    Homogeneous exterior gateway protocol (why?)
  Nodes in the routing table are ASMs (in principle but not in practice, we discuss this later)
  Main goal: reachability

## Slide 6: Standard Interdomain Routing Protocols
General aspects
  Very complex and difficult
  Large scale (140,000 network prefixes in the core of the network, and about 14,000 AS numbers)
  Focuses on reachability rather than optimality
  Must be loop-free
  Specify how reachability information should be exchanged

## Slide 7: Old Tree-Structure
Internet before 1990 had a tree-structure
Main “core” was the NSF Backbone (NSFNET)
An AS could have a parent and/or children
No “peering”, strictly hierarchical.
A low level AS could have a default route to its parent (and thus need not know the whole Internet).
However, the NSFNET needed to know the whole Internet
NSFNET backbone
Stanford
BARRNET
regional
Berkeley
P
ARC
NCAR
UA
UNM
W
estnet
regional
UNL
KU
ISU
MidNet
regional
…

## Slide 8: EGP (old, not used anymore)
Defined on the Internet having a tree structure
Embodied (and enforced) tree structure
Each AS must learn how to reach every AS in its sub-tree
Thus, the core network learns the path to every AS
Had to be replaced eventually

## Slide 9: Privatization of the Internet
Backbone service provider
Peering
point
Peering
point
Large corporation
Large corporation
Small
corporation
“
Consumer
”
ISP
“Consumer” ISP
“Consumer” ISP
Mid 1990’s, NSF relinquished control of the Internet backbone
We have many commercial backbone providers (UUNet/Worldcomm, Sprint, MCI, ...)
Mesh connectivity, multi-homed networks,
Loops galore
Need a new solution

## Slide 10: Types of AS
Stub: only connected to one other AS; carries local traffic only (can use default path to its parent AS, and does not necessarily have an AS number)
Multi-homed: connected to multiple ASM’s, but refuses to carry transit traffic
Transit: allows traffic from other ASM’s to cross it.
Need a protocol that can handle this general connectivity

## Slide 11: Reachability vs Optimality
Each domain can choose its own interior routing protocol (also known as interior gateway protocols IGP)
It can choose any scheme to assign metrics (e.g. costs, bandwidth, etc) to its interior links
No consistency between ASM’s
  Metric of 1000 in one AS may be great, but awful at another (it may not even be the same type! E.g. cost vs bandwidth)
Impossible to find the least cost path to a destination AS.
Best you can do is find “a path”.
Each AS advertises “network reachability information”
  I can reach AS n and it contains networks 129.18.0.0/16, 100.18.0.0/16
  No cost is given.

## Slide 12: Need for Loop Freedom
Short-lived or long-lived routing loops are devastating
  The traffic of an entire AS could be interrupted
  Looping packets would cause congestion
Example
  Assume we were using DV routing, and to reach AS0, a loop formed between AS2, AS3, AS4, back to AS2
  All traffic originating from these three ASMs goes around, wasting bandwidth!
AS1
AS2
AS3
AS4
AS0

## Slide 13: Need for Flexible Routing Policies
Each AS is not forced to disclose its reachability
  Multi-homed ASM’s prevent through traffic by not announcing reachability
Domains should have the freedom to choose their path to each destination domain
  An AS may prefer a neighboring AS according to:
    Some economic relationship
    Level of trust (may not trust some ASM’s)
The whole point is to find a “good” path, not an optimal one, that you “like”

## Slide 14: Why not DV or Link-State?
Link-State
  Too much overhead: O(N2) message and processing overhead
  Even for intradomain routing, it has too much overhead
Distance Vector
  Slow to converge: counting to infinity.
Need for flexible policies
  Neither of the above two supports flexible policies.
    You must know the entire path taken by your neighbor to decide if you want it or not
    Must selectively advertise routes to different neighbors

## Slide 15: BGP-4
Current standard interdomain routing protocol
Assumption
  Internet is an arbitrarily interconnected set of ASM’s
Each AS has
  Border routers (one or more)
    Connect an AS to the Internet
    Used for default external routing
    Usually is a BGP speaker
  BGP speakers (one or more)
    Routers that participate in the inter-domain routing protocol
Note: Routers that are not BGP speakers only learn about networks within their AS
  I.e., they only run OSPF, RIP, etc; an intra-domain protocol.

## Slide 16: BGP-4
Neither link-state nor distance-vector
BGP speakers advertise, for each network N
  The full path (list) of ASM’s to reach network N
Loops are avoided by not choosing a neighbor’s path if it contains your own AS ID.
Only one path is advertised even if many are available.
  Advertise the route that you have chosen according to your routing policies.

## Slide 17: BGP-4 Route Advertisements
Example
  AS10 advertises to its neighbor (AS6) that 131.141 and 192.10.20 are local to AS10
  AS6 advertises to its neighbors (AS19, and AS18) that 131.141 and 192.10.20 are reachable via the path (AS6, AS10)
  AS19 advertises to its neighbors (not drawn) that 131.141 and 192.10.20 are reachable via the path (AS19, AS6, AS10)
AS10
AS18
AS19
AS6
131.141
192.10.20

## Slide 18: Multiple BGP Speakers per AS
Two types of neighbors (peers)
  Internal: in the same AS, use iBGP protocol
  External: in a different AS, use eBGP protocol
“neighbors” may be multiple hops from each other.
Full (reliable) TCP connectivity between internal neighbors (peers).
  All internal neighbors share the routes they learned from outside ASM’s.
Information is not “refreshed”
  Only “keep-alive” messages are sent periodically to each neighbor.
  Advertised paths, if no longer existent, must be withdrawn explicitly.
  Thus, a router has to explicitly tell its neighbors a path is no longer available.

## Slide 19: Why is everything more scalable?
Recall, two levels of the hierarchy
  Within an AS (intradomain)
  Outside of an AS (interdomain)
Within an AS, finding a good interdomain route boils down to finding a path to the right border router (only a few per AS)
Outside of an AS, you are only aware of other ASM’s and which networks they contain, not how they are structured inside (plus there is aggregation due to CIDR).

## Slide 20: Integrating Intradomain and Interdomain
Customer AS: how to reach the Internet? (outside world)
  It is a stub AS
  The border router “injects” a default entry 0.0.0.0/0 into the intradomain protocol (e.g. OSPF or RIP)
  This causes all traffic from the customer to the outside to be sent via the border router to the service provider
AS10
AS18
AS19
AS6
Customer
Service Provider
Backbone Network
131.141/16
192.10.20/24
128.140/16
182.10/16

## Slide 21: Integrating Intradomain and Interdomain
Service Provider AS6: how to reach customer networks?
  Assume it has both BGP speakers and non-BGP speakers.
  In AS6, the router bordering with AS10 learns of 131.141/16 and 192.10.20/24 through the border router of AS10 (BGP)
  In AS6, the border router with AS10 “injects” into AS6’s intradomain protocol that it has a “direct link” to networks 131.141/16 and 192.10.20/24
  In AS6, any non-BGP speaker router will reach 131.141/16 and 192.10.20/24 via the border router with AS10.
  What does the BGP border router in AS6 advertise to its peer in AS19?
AS10
AS18
AS19
AS6
131.141/16
192.10.20/24
Customer
Service Provider
Backbone Network
128.140/16
182.10/16

## Slide 22: Integrating Intradomain and Interdomain
Backbone networks:
  Too many prefixes to inject into intradomain protocol
  All routers speak BGP
  Via the iBGP protocol, they share their reachability information (paths to each AS and the networks of each AS)
  To reach a specific network,
    iBGP says which border router is needed, and
    the intradomain protocol (e.g. OSPF) gives the next hop to this router.
AS10
AS18
AS19
AS6
Customer
Service Provider
Backbone Network
128.140/16
182.10/16
131.141/16
192.10.20/24

## Slide 23: BGP Import, Export, Path Selection
There are three types of policies:
  Import Policy: of the paths offered by my neighbours, which ones will I allow? (i.e. “import” the path)
  Path Selection: given the paths offered by my neighbours which satisfy my import policy, which one do I like the best?
  Export Policy: given my current path, will I tell my neighbour of this path or tell my neighbour that I have no path? (i.e., “export” the path)

## Slide 24: Route fields
Assume an AS A receives a route (path) r from its neighbour B
Route r has several fields
  r.as_path: the list of ASms from B to the destination
  r.MED: if multiple links between A & B, MED determines which one B prefers that A uses (multi-exit discriminator)
  r.community: you can organize ASms into “communities”, and mentioned the community to which this path belongs.
  r.local_pref: how desirable the path is (local preference), and is assigned by A.

## Slide 25: Path Selection Policy
If we have multiple BGP speakers per AS then, path selection is as follows:
  From the paths that satisfy the import policies
    Choose those with the greatest (largest) local_pref
  Then, out of the remaining paths from above choose the ones with least # of AS hops to the destination
  Then, for each neighboring AS B,
    Of the paths chosen above, if multiple paths from B (one per BGP border router), choose the one with lowest MED value (we left at most one path per AS neighbor)
  Choose the path whose internal cost to reach the border router is least.

## Slide 26
smaller

## Slide 27: Answer to previous slide
Path via (A1, U2) is discarded due to its low local preference value of 1 (all other paths have a local pref value of 2)
Next, paths via AS V are also discarded because # AS HOPS is larger than the other ASms
We are left with 3 paths: (A1,U1), (A3,W2) and (A3,W1)
(A3, W2) is discarded since its MED is greater than (A3,W1)
We are left with two paths (A1,U1) and (A3,W1).
Then, A1, A2, and A3 choose their path according to the internal cost to reach the border router
  A1 chooses to go via U1, since reaching the border costs 0 (cost from A1 to A1 is zero, but from A1 to A3 is > 0)
  Similarly, A3 chooses to go via W1
  A2 chooses to go via A1 or A3 depending on which one is closer (in terms of local cost) to A2.

## Slide 28: Problems with BGP
Instability
  Route flapping
  Arbitrary path decisions can lead to bouncing/loops
  Not guaranteed to converge
Over 100,000 network prefixes in some routers (without using defaults)

## Slide 29: Back to Subnetting: Summary
One network number is given to an organization
The organization divides the network number into “subnets”, and assigns each subnet to a different physical network in the organization.
Pros
  Helps address consumption – one “network number” spread out over multiple “subnets” (physical network)
  Helps reduce routing table size of routers outside the organization – one network # per organization

## Slide 30: Subnetting Summary
Problems remaining
  Does not reduce class B address space pressure (organizations need more than the 255 hosts of a class C address)
  If you give multiple class C addresses to an organization, core routers will have LOTS of networks in their routing tables.

## Slide 31: Solution – Classless Interdomain Routing (CIDR)
Eliminate class notation (no more A, B, C)
“Networks” no longer exist, we have now “address blocks”
For historical reasons, the word “network” is still used.
Consider the address block from:
This is actually represented by the “network” number 192.4.16.0 (32 bits long) and a prefix length of 20 bits
192.4.16.0/20
0
1
0
0
1
1
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
0
1
0
0
1
1
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
to:
0
1
0
0
1
1
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
i.e. (x = “bits not in the network #”, set to zero by standard convention)
0
1
0
0
1
1
0
0
0
0
0
0
0
0
0
0
0
0
0
1
X
X
X
X
X
X
X
X
X
X
X
X

## Slide 32: E.g., Address provider block
A service provider could be assigned the address block 192.4.0.0/16
It advertises to all its neighbors that it can reach any destination whose IP address is within this block
  I.e. it advertises 192.4.0.0/16 to all its neighbors.
0
1
0
0
1
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
Service Provider: 192.4.0.0/16
Mask 255.255.0.0 (16 bits)
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0

## Slide 33: Breaking the address block
The service provider may have many clients.
It further breaks its address into contiguous blocks of addresses and gives a block to each of its client organizations.
One of them is 192.4.16.0/20 for client organization X and another is 192.4.128.0/17 for client organization Y
Routers outside the service provider have only a single entry for the entire service provider, I.e., 192.4.0.0/16
0
1
0
0
1
1
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
Mask 255.255.240.0 (20 bits)
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
0
0
0
0
1
1
1
1
0
0
0
0
0
0
0
0
Organization X: 192.4.16.0/20
0
1
0
0
1
1
0
0
0
0
0
0
0
0
0
0
1
0
0
0
Mask 255.255.128.0 (17 bits)
Organization Y: 192.4.128.0/17
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0

## Slide 34: Multiple advertisements
Service Provider advertises block 192.4.0.0/16 to all its neighbors
Client X of the service provider may have neighbors other than its Service Provider (e.g. X and Y could be neighbors)
Client X of the service provider advertises block 192.4.16.0/20 (more specific block) to all its neighbors
Note that the advertisement of the Service Provider subsumes the advertisement of X.
More on this later.

## Slide 35: Further Breaking of Address Block Inside the Domain
Organization X has multiple Ethernet networks
Each one requires an address block
X was given 192.4.16.0/20
One Ethernet has 300 hosts
X assigns it the block 192.4.18.0/23
Routers within X advertise the block 192.4.18.0/23 to other routers within X
0
1
0
0
1
1
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
Mask 255.255.240.0 (20 bits)
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
0
0
0
0
1
1
1
1
0
0
0
0
0
0
0
0
Organization X: 192.4.16.0/20
0
0
0
0
0
0
0
0
0
1
0
0
1
1
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
1
0
Mask 255.255.254.0 (23 bits)
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
0
0
0
0
1
1
1
1
0
0
0
0
0
1
1
1
Ethernet within X: 192.4.18.0/23
0
0
0
0
0
0
0
0

## Slide 36: CIDR Summary
Generalize subnet notion and subnet masks (just mask).
Allow only contiguous masks
The mask is dynamic
Specify network by <network #> / <# of bits in mask>
As you get closer to the destination, the mask size “increases”, I.e. more details are available.
Aggregate routes in routing tables – contiguous blocks of network numbers along the same path are aggregated into one network with a smaller mask.

## Slide 37: CIDR vs Subnetting and Supernetting
Subnetting
  Share one address (A, B, C network number) across multiple physical networks
Supernetting
  Aggregate multiple addresses (multiple C network numbers) for one physical network/organization
CIDR
  Accomplishes both under a common framework
  Class addresses (A, B, C) no longer exist (unless the system is old)

## Slide 38: Longest Match Prefix (weird)
Assume a service provider P has a contiguous group of addresses.
This group was split into different organizations, X, Y,Z, etc.
What if X changes to service provider Q? Its IP addresses would change (bad, lots of renumbering)
X is allowed to keep its IP addresses.
P advertises to outside routers that it can reach the contiguous group of addresses (including X!)
Q advertises the more specific group of addresses of X.
Routers must follow path to Q, since Q has more “specific” information (longest prefix).

## Slide 39: CIDR
Trend is for increasing amounts of overlap in routing table entries
Example: 128.174.142.200
  Matches second, third and fourth lines
  Route to entry with longest match
Subnet # / length | Next Hop
128.174.141.0 / 24 | Interface 0
128.174.142.192 / 27 | Interface 1
128.174.142.128 / 25 | R1
128.174.0.0 / 16 | R3
Default | R3